Press information

To download a 300dpi print quality image,

go to parkfield.co.uk/hammond-canada/c2-seismic-print.jpg

To download a Word file of the text, go to parkfield.co.uk/hammond-canada/c2-seismic.doc
To view all Hammond Manufacturing press information, go to parkfield.co.uk/hammond-canada/

Hammond’s popular C2 19” rack rated for 1000 lb load in extreme SDC E seismic environments

Released February 21, 2017

Independent testing has confirmed that Hammond Manufacturing’s welded frame construction C2 19” rack, hammfg.com/dci/products/cabinet-systems/c2, available as standard in sizes from 20U high, 23” wide and 23.62” deep to 49U high, 23” wide and 36” deep is suitable for use in all USA locations including the highest Seismic Design Category, SDC, E, which covers most of the western seaboard. Typical applications include broadcast, test equipment, cabling cabinets, systems and general electronics.

The C2 19” rack is rated to carry a 1000 lb load when installed in building sited on Soil Groups A, hard rock, down to D, stiff soil. To conform, the centre of mass of the load must be below the height centerline of the rack and the rack must be bolted to the floor of the building. The doors and panels are not structural elements, so the seismic rating applies to both open and clad racks.

The C2 19” rack is constructed from a 14-gauge steel fully welded frame, fitted with 16-gauge steel doors and side panels and for 19” equipment mounting, there is a choice of either 10-gauge steel tapped mounting rails or 12-gauge steel square hole mounting rails. The mounting rails are fully adjustable front to back within the rack to accommodate differing equipment depths. A choice of top panels include Solid, Vented, Solid with Fan cutouts or Solid with Pre-installed Fans up to 550 CFM. A comprehensive range of dedicated accessories ensure that the great majority of projects and applications can be satisfied by configuring the rack from standard products. The C2 19” rack can be easily and quickly factory modified if required.

*** Ends: body copy 267 words ***

Notes to Editors.

For further information:

Ross Hammond

Hammond Manufacturing Co. Ltd.

Electronics Group

485 Conestogo Road

Waterloo

Ontario N2L 4C9

Canada

Telephone: 519.886.7170

Fax: 519.886.8311

rnhammond@hammfg.com

www.hammondmfg.com

Agency contact:

Nigel May

Parkfield Communications Limited

Parkfield House

Damerham

Hants

SP6 3HQ

UK

tel: + 44 1725 518321

fax: + 44 1725 518378

nigel.may@parkfield.co.uk

www.parkfield.co.uk

Hammond is one of the world's leading manufacturers of small plastic, die-cast and metal enclosures for use in the electronics, electrical and allied industries.