Press information

To download a 300dpi print quality image, go to http://www.parkfield.co.uk/verotec_uk/diplomat1-print.jpg

Diplomat 19” desktop and caseframe enclosures

Released 14 March 2011

The field-proven Diplomat family from Verotec is an elegantly styled enclosure, available as a 19” or 10.5” wide thermally managed, EMC capable unit suitable for housing stand-alone systems, as a 19” caseframe for direct mounting of boards and modules and as a vertical tower unit. Manufactured as standard in 3U, 4U, 6U and 9U heights and depths of 322, 422, 522 and 622mm, the Diplomat is particularly suitable for medical technology application, the research environment and as the housing for a wide variety of desktop instruments.

With power densities steadily increasing, effective ventilation is of paramount importance. All horizontal cases and caseframes can be fitted with a filtered ventilation plinth that replaces the standard base cover. The plinth can be fitted with fans to push air into the unit or it can provide increases air throughput if fans are mounted in the rear panel to draw air out of the case. The cool air is directed through the active equipment area by a duct plate that blanks off the space behind circuit boards.

For applications that require enhanced EMC attenuation, both cases and caseframes are available as Diplomat-RF versions, which, while externally identical to the standard units, include beryllium copper finger gaskets that can be fitted to the top and bottom covers at variable spacing depending on the attenuation level required.  EMC panels and, for ventilated plinth versions, an alternative finely pierced base cover, enable attenuation of levels of around 100dB at 1MHz to be achieved.

Optional extras include a range of transparent front doors, formed from strong, shatterproof tinted acrylic. The "U" section lockable doors can be vertically or horizontally hinged and incorporate coloured styling trims. Also available are rear bump down feet, a heavy-duty carry handle, telescopic slides for subrack/chassis mounting in the 19" case versions and carpet gliders for the tower versions.

*** Ends: body copy 305 words ***

Notes to editors.

For further information:

Tim Armstrong

Verotec Limited

Unit E

Eagle Close

Chandlers Ford Industrial Estate

Eastleigh

SO53 4NF

tel: + 44 (0)2380 246900

fax: + 44 (0)2380 246901

sales@verotec.co.uk

www.verotec.co.uk

Agency contact:

Nigel May

Parkfield Communications Limited

Parkfield House

Damerham

SP6 3HQ

tel: + 44 (0)1725 518321

fax: + 44 (0)1725 518378

nigel.may@parkfield.co.uk

www.parkfield.co.uk