Press information

To download a 300dpi print quality image,

go to http://www.parkfield.co.uk/bvm/ad-modules-print.jpg

For all BVM releases, go to http://www.parkfield.co.uk/bvm

Low cost isolation and converter modules for Industrial PCs

Released 21 February 2012

The BVM Group has available three modules that increase the capability and versatility of the company’s latest Mini-ITX, 3.5” and 5.25” format industrial grade motherboards; physically mounted on PC I/O brackets, they are also compatible with many older models. The modules are designed to interface with the GPIO from the Winbond chip and provide electrical isolation and protection.

The ADP-GPION four-way or eight-way modules feature photodiodes and high current relay interfaces on each line to isolate the motherboard from potential damage caused by Electrostatic Discharge (ESD) voltages and other transients on lines that interface with the GPIO controller chip. GPIO peripherals vary quite widely. Software controlled, they vary from a group of pins that can be switched as a group to either input or output or each pin can be set up to accept or source different logic voltages, with configurable drive strengths and pull up/downs. With voltages as low as 10V able to damage semiconductors, this issue is increasingly significant when embedded motherboards are incorporated in industrial control equipment, kiosks and other systems. As a separate but related introduction, a new software utility, which gives easy access to the GPIO bits and the watchdog timer, is available to simplify programming of the Winbond GPIO chip used on many motherboards.

The AS-RS485 converts two RS-232 ports to two RS-485 ports. Requiring only a 5V DC input, this board provides complete galvanic isolated and features full duplex RS485 transceivers. RS485 uses differential signals and is ideal for systems where the ground loop is broken allowing for large common mode voltage variation.

*** Ends: body copy 262 words ***

Notes to Editors.

Technical and sales contact for publication:

David Harding

BVM Limited

BVM House

Hobb Lane

Hedge End

Southampton

SO30 0HG

t: + 44 (0)1489 780144

f: + 44 (0)1489 783589

sales@bvmltd.co.uk

www.bvm-store.co.uk

Editorial contact:

Rod Clarke

t: + 44 (0)1489 780144

rod_c@bvmltd.co.uk

Agency contact:

Nigel May

Parkfield Communications Ltd

Parkfield House

Damerham

Hants

SP6 3HQ

t: + 44 (0)1725 518321

f: + 44 (0)1725 518378

nigel.may@parkfield.co.uk

www.parkfield.co.uk